## Slide 1: Project: On-Board Diagnostics Monitoring

## Slide 2: Project Problem
Design an in-vehicle system to collect and transmit data from the OBDII (on-board diagnostic II system) that does not require a constant connection

## Slide 3: Goals (1)
The goal is to design and develop a hardware and software solution for collecting, storing, and Transmitting data from the OBDII of a car, to a backend server; and providing the remote users access to the collected data through a mobile or web application.

## Slide 4: Goals (2)
The goal is accomplished by:
  Connecting the RPi to the OBDII and gathering, filtering and saving data
  RPi connecting to Wi-Fi when available
  Sending saved data to the database located on a server
  Providing access for remote users to retrieve data (through mobile or web applications)

## Slide 5: System Overview
Database
Data Acquisition unit
Hardware:
Raspberry Pie 3
Mobile Application
(iOS/Android)
Web Application
or
Unit 1
Unit 2
OBD II
emulator
Unit 3

## Slide 6: System Specification (2)
1) Data Acquisition System
  Given: Requirement Document
  To Do: Design of software residing on RPi
2) Database System
  To Do: Design of a stand-alone database for storing the data collected from RPi unit
3) User Interface
  To Do: Web Application or mobile application design

## Slide 7: Data Acquisition System
System hardware path
Unit 1
Unit 3

## Slide 8: System Configuration
The On-Board Diagnostics & Monitoring System is composed of three subsystems:
  Data acquisition
  User interface
  Database
Unit 1
Unit 2
Unit 3

## Slide 9: System Configuration
Subsystem 1: Data acquisition

## Slide 10: Subsystem 1. Data Acquisition
The OBDII connects physically to the RPi through an appropriate cable
The RPi filters input prior to being stored
The RPi will store:
  Vehicle speed (RPM); Vehicle ID; Time Stamp; Fuel Pump Status (P1230 to P1239); Engine RPM or Speed limit reached (P1270); Seat belt status (B1426 to B1430); ABS status (C1095 to C1103)
The RPi must write filtered OBDII data to a micro SD card
The RPi must be able to connect to a wireless access point
The RPi must be able to transfer filtered OBDII data to a backend server
The system SD card is removable and replaceable
The system must read an inserted SD card after start up
The system will be compatible with a Ford F150 vehicle
The RPi is powered through the vehicle electric system

## Slide 11: Subsystem 2. User Interface
The Android application asks the user for its vehicle id to retrieve and save information for a single vehicle at a time
The Android application connects to the database to retrieve records corresponding to the vehicle
The Android application displays the following information:
  Time Stamp; Fuel Pump Status (P1230 to P1239); Engine RPM or Speed limit reached (P1270); Seat belt status (B1426 to B1430); ABS status (C1095 to C1103)
The Android application gathers GPS location information (from the smartphone) while the vehicle is moving
The Android application gathers information on a second by second basis including:
  Time; Latitude; Longitude
The Android application sends this data to be saved in the database

## Slide 12: Subsystem 3. Database
The database is stored in a web server connected to the internet and allows remote connections from users
The database is able to store the data received from the RPi
The database is able to store data received from the Android App
The RPI is able to transfer stored data to a server database with an associated vehicle id
The database allows the Android client to perform queries

## Slide 13: Subsystem 1: Configuration

## Slide 14: Subsystem 2: Configuration

## Slide 15: Subsystem 3: Configuration